## Slide 1
Celluer Automated External Defibrillator

## Slide 2
CONTENT
CAED BATTERY
  OREL Battery Specifications
  Battery manufacture
0
CAED Circuit
  High voltage Board
    Charging Circuit
    Capacitor
    H-Bridge circuit
    Inner selector
    Internal Discharge circuit
    Outer selector
    Connector
Control Board
  PSOC
  Inputs/Outputs
APP

## Slide 3
CAED
OREL Battery Specifications
Type: Lithium Manganese Dioxide
  high-energy
  long-lasting battery
Voltage: 9 volts
Capacity: 4.2 ampere-hours (Ah)
Weight: 1.5 pounds (0.68 kg), or below
Size: 13.34 cm x 9.53 cm x 3.81 cm or below.
Shelf life: 2-4 years
Operating temperature range: temperatures ranging from 32°F (0°C) to 122°F (50°C).
Charging time: The battery can be fully charged in under four hours
Run time: minimum of 200 shocks or four hours of monitoring

## Slide 4
Battery Manufacturer
Lithium manganese dioxide
4 Batteries
9v nominal voltage
1200mAh
$500 for 1 battery

## Slide 5
Circuit Diagram
20

## Slide 7
High Voltage Board
20
HV-B contains the circuitry necessary to perform defibrillation
capacitor, used to store the energy to be released to the patient
charging circuit, which rapidly charges the capacitor
H-Bridge circuit, required to perform biphasic defibrillation
internal discharge circuit, used to dump the unused residual energy ( discharge capacitors)
two selectors, used to isolate the patient from the capacitor, and to route the ECG signal to the C-B.

## Slide 8
Charging Circuit
Charging Circuit Self oscillating fly back convertor
The purpose of the CAED charging circuit is to charge the high-voltage capacitor to store the energy needed to deliver an electrical shock to the heart in case of cardiac arrest.

## Slide 9
Charging Circuit
LM358 OP AMP -accurate and stable control of the charging process.

## Slide 10
Capacitor
Nesscap ESHSR-001R5C4R6N
Type of ultra capacitor(super capacitor)
Design to store and release high amount of energy quickly
Low ESR ( Equilent series resistance
High power density

## Slide 11
Capacitor

## Slide 12
H- bridge circuit

## Slide 13
Internal discharge circuit
Deliver the high-energy electrical shock to the heart by discharging the charged capacitor of the AED in a controlled manner.

## Slide 14
Electrode Connectors: These connectors allow the user to attach the electrode pads to the AED device.
Selector Buttons: ex - select the language of the voice prompts
- switch between adult and child modes.
Battery Connector
Connectors & Selectors

## Slide 15
Power Switch: AED on and off.
Shock Button
Connectors & Selectors

## Slide 16
Microprocessor: Brain of the device.
Electrodes: These are the pads that are attached to the patient's chest to deliver electrical shocks.
Input /outputs interfaces
Audio system: The control board manages the audio output of the device, including voice prompts and warnings.
Control board

## Slide 17
Control board
HC-O5 Bluetooth module
Audio module DFPlayer mini module

## Slide 18
  Operational check (Sound message) system
  ECG History
  ECG Report (present )
APP
Operational Check
Exit clinical mode
Operational check summary
Run operational check
Auto test summary
Exit
YES
NO

## Slide 19
Operational check
Reference number 1st step
Serial num 2nd step
Last operational check Date/(pass/fail)
General system test: in progress pass
Therapy Knob : pass
Charge button : pass
Shock button : pass
Audio test : pass
Therapy delivery test : pass /external /paddles
Leads ECG test : pass ECG cables
Pads/paddles/ECG test : pass external paddles
Battery test : pass
Printer test : pass
Instruction messages (with sound message system)